THE OVERALL PROCEDURE

- The sample is of arbitrary Shape.

- Obtain a set of x, y, z coordinate values, which when tabulated can conveniently provide the reconstruction of the shape of the specimen. This could be a laboratory experiment (as described in Sheets #11 and #12 in this poster display) which has to be standardized by considering the specimen of typical shapes and the requirements for the Calculation of bulk susceptibility effects as described in Sheets #7 and #8 of this display.

- Orient the specimens and make the HR PMR measurement to obtain the rotation pattern. Compute for the Principal Directions and Component values of the measured Shielding Tensor.

- Calculate the inter-molecular contribution to shielding tensor by discretely summing within a semi micro volume element as described in Sheets #2, #3, #5. Subtract this inter-molecular contribution from the measured experimental Tensor values.

- Calculate the shape-dependent values due to the bulk susceptibility effects as described in Sheets #7 and #8. Subtract this calculated tensor for shape dependent contributions from the result of step 4 above.

- The value of the tensor obtained as a result at stage 5 should be the required INTERMOLECULAR SHIELDING TENSOR.